## Slide 1
FMCC Engineering
Jul, 2019
Trouble Shooting for Portable

## Slide 2
Sensor Issue
Error code: E1,E2,E3
Error
Check the sensor is good or not?
Error
Well connected the sensor and PCB
Replace the bad sensor
Check the connection port between sensor and PCB is loose or not connected
Check PCB
Sensor is open circuit?
Sensor is short circuit?
Component damaged?
Any other material inside the display board? Wet? Wet?
Replace IU chip or PCB
Room temp. sensor
Indoor coil middle temp. sensor
Outdoor coil outlet temp. sensor
Indoor temp. sensor abnormal
OK
OK
Error
Power off and restart the system 3 minutes later to check the error remain or not

## Slide 3
Display panel communication error(E4)
Error code: E4
Error
Check the display board?
Error
Well connected the sensor and PCB
Replace the display board
Check the connection port between display board and PCB is loose or not connected
Check PCB
Component damaged?
Any other material inside the display board? Wet?
Component damaged?
Any other material inside the display board? Wet?
Replace main PCB
Display board communication error
OK
OK
Error
Power off and restart the system 3 minutes later to check the error remain or not

## Slide 4
Leakage protection (EC)

## Slide 5
Thanks!